BEAR LAKE COUNTY BUILDING DEPARTMENT

Building Official

Wayne Davidson

PO Box 190

7 East Center, Paris. ID. 83261

208-945-2212 Ext 39

blbuilding@dcdi.net

July 12, 2017

Bear Lake County is seeking bids for a storage building.

All building components and foundation shall comply with the 2012 International Building Code. Snow, wind, seismic, and exposure loads shall meet or exceed Bear Lake County requirements set by ordinance.

The building will be within the city limits of Paris, on the grass land directly east of the city post office. Access to the building will be from 1st North in Paris. Bear Lake County will acquire all city building permits and utilities permits.

This building shall be 100’ X  50’, made of steel with accompanying engineering,  on an engineered foundation designed for the steel structure above it. The building will have a single sloped roof, sloping to the rear of the building.

The building shall be divided into four compartments or bays, each one having an exterior metal man door of 6’8” X 3’ with individually keyed knobs. Each bay shall have a garage door, with one bay having two doors. The bays will be divided up as;

Sheriff’s boats, approximately 36’ X 49’ with a single man door, and two garage doors each 14’ wide by 14’ tall.

Mobil Command Unit, approximately 22’ X 49’ with one man door and one garage door 14’ wide by 14’ tall.

Ambulance approximately 20’ X 49’ with one man door and one garage door 14’ wide by 14’ tall.

Fire Truck, approximately 20’ X 49’ with one man door and one garage door 14’ wide by 14’ tall.

A wood, 2” X 4” wall separating the four bays will extend from floor to ceiling, and be covered on each side with ½” wafer board.

There will be bathroom in the far corner of the Sheriff’s Boats bay, in the exterior corner. Its size will be 6’ X 5’. Plumbing for toilet and sink will be installed in the floor. The interior walls and fixtures will be completed by county employees.  An exterior door will access the room from the end wall.

All garage doors will be commercial grade with automatic openers with remote. Garage doors will have a window panel in the door at or above the 8’ level.

All walls and ceilings will be insulated. Roof R19 walls R13 minimum.

The floor will be finished concrete, 5” thick minimum more if engineering requires, sloped to the opening and cut.  Each bay will have a floor drain adequate for ice and water from vehicles. There will be a 5’ concrete apron along the length of the front of the building. Outside of each garage door, at each edge of the door, will be a 4” steel bollard filled with concrete.

There will be a frost free water hydrant connected to city water, outside the building on one end.

Each bay will be wired for electric lighting with switches.

The Sheriff’s boat bay, the Ambulance bay and the Fire Truck bay will have a ceiling hung propane heating unit capable of maintaining the room temperature to 50 degrees. Each with its own thermostat. The heating units in each bay will be independent of the others, each with its own propane tank or meter. The building will have gas line run to each bay for future needs.

Along with the construction bid estimate, interested contractors must provide an Idaho Public Works license number, and earliest possible start date.